## Slide 1: Carbon Capture & Storage
Energy & Climate Mini-Workshop
Howard Herzog
MIT
November 3, 2008

## Slide 2: The MIT Coal Study
Released March 14, 2007
  On web at mit.edu/coal
We conclude that CO2 capture and sequestration (CCS) is the critical enabling technology that would reduce CO2 emissions significantly while also allowing coal to meet the world’s pressing energy needs.

## Slide 3: MIT Coal Study Summary of Key Takeaways
Technology readiness is critical – there are myriad options to pursue.
Don’t preclude options by anointing winners prematurely.
We need to drastically increase R&D to bring CO2 capture technologies to fruition. There is urgency to move ahead now if we are to reach Gt scale by 2050. Large scale demonstration projects are key.
No showstoppers, but moving from the Mt scale to the Gt scale is a major challenge.

## Slide 4: Technological Readiness
All major components of a carbon capture and sequestration system are commercially available today.
However, integrated, large-scale CCS systems are not “commercially available”
  One stop shopping
  Subsurface vendors
  Guarantees

## Slide 5: Two biggest challenges for CCS
Reducing costs primarily associated with capture
Reducing uncertainties primarily associated with storage at scale

## Slide 6
Source: ABB Lummus
CO2 Capture at a Power Plant

## Slide 7: Capture and Compression Capital Costs
Power Plant | Capture Technology | Capital Investment | Power Output | $/kW
SCPC | Post- Combustion | +23% | -24% | +62%

## Slide 8: CCS, Power Plants, and Costs
Costs have gone through the roof over the past few years
Market volatility makes costs estimation difficult
Given new reality, expectation is for a cost correction, but to where?

## Slide 9: Cost Indices

## Slide 10: Cost of Capture/Compression
 | Units | Reference Plant | Capture Plant
Total Plant Cost | $/kW | 1910 | 3080
CO2 Emitted | kg/kWh | 0.83 | 0.11
HHV Efficiency | % | 38.5 | 29.3
Cost of Electricity | $/MWh | 62.6 | 100.3
CO2 Avoided Cost | $/tonne |  | 52
Notes:
2007 $
Nth plant
Based on supercritical pulverized coal
Does not include transport/storage

## Slide 11
Coal w/CCS: IGCC w/ pre-combustion CCS @ HR=10942 Btu/kWh, Illinois#6 Coal @
$1.79/MMBtu, 90% Capture, 80% CF, 0.109 kg/kWh emissions rate;
Gas: CCGT @ $950/kW, HR=7000 Btu/kWh, 65% CF, 0.368 kg/kWh emissions rate
Projected Capex
$3000-4000/kW
2007 Avg. Delivered
Price $7.37/MMBtu
Breakeven Capex for Coal w/CCS versus CCGT

## Slide 12: Challenges for Commercialization
Costs
Infrastructure
Regulatory Framework
Long-term Liability
Subsurface Uncertainty
  Capacity
  Long-term Integrity

## Slide 13: Moving forward
New capture technologies
Large-scale demos

## Slide 14: Capture Technology Pathways
 | Plusses | Minuses
Post-Combustion | Compatible with existing infrastructure; retrofits; flexibility | Current methods have high energy penalties
Oxy-Combustion | Potentially less expensive than post-combustion; retrofits | Cost of oxygen; lack of experience
Pre-Combustion | Projected lowest incremental cost for capture | Slow progress of IGCC

## Slide 15: CO2 Storage
Current evidence indicates that it is scientifically feasible to store large quantities of CO2 in saline aquifers
In order to:
  Address outstanding technical issues that need to be resolved to confirm CCS as a major mitigation option
  Establish public confidence that large scale sequestration is practical and safe
it is urgent to undertake a number of large scale (on the order of 1 Mt/yr injection) experimental projects in reservoirs that are instrumented, monitored, and analyzed to verify the practical reliability and implementation of sequestration. None of the current sequestration projects worldwide meets all of these criteria
MIT Coal Study – Finding #5

## Slide 16: Cancellations of Major Demonstration Projects
May 2007 – BP Petershead (Scotland)
June 2007 – Shell/Statoil Draugen (Norway)
Sept 2007 – Saskpower (Canada)
Jan 2008 – FutureGen (US)

## Slide 17: Critical Question
Is it reasonable to expect to build 100s of coal-fired power plants with CCS by 2050 when we are having so much trouble building just one today?

## Slide 18: Emissions Performance Standards
California standard is 1100 lbs CO2 / MWh
Costs
  Similar to full capture in $/ton
  Total cost is less (i.e., less tons captured)
For both post- and pre-combustion, less changes required in power plant
Overall environmental performance similar to natural gas
Allows early implementation and can be a good source of CO2 for storage demonstrations
Will be competitive at higher natural gas prices

## Slide 19: Contact Information
Howard Herzog
Massachusetts Institute of Technology (MIT)
Energy Initiative
Room E40-447
Cambridge, MA 02139
Phone: 617-253-0688
E-mail: hjherzog@mit.edu
Web Site: sequestration.mit.edu